Seafish Suggested Control Documents for the use of Ozone

Annex 1

Residual Ozone Monitoring Record Sheet

Prior to using ozone in any system that will hold bivalves the following procedure must be complied with.

- Check the calibration record sheet for the instrument or method of sampling. Should the instrument or method proposed to be used not have been calibrated within the last 6 purification cycles do that now.

- Take a 2 litre sample of the seawater that will be used to immerse the bivalves in and record the oxidative redox potential (ORP) three times at five minute intervals. Calculate the average for the three readings. This is now your ORP baseline figure (ORPBF).

- The ORPBF + 10% in mV’s is your ‘Action Point’. Any reading measured above this level should result in an immediate action protocol being followed including shutting down the ozone generator or its feed line to the purification system in question.

- Record the amount of Ozone being generated and the ORP at the spray bar or where the water enters the purification tank and also at the suction bar or where the water leaves the purification tank. Do this one hour after the purification cycle starts, about half way through the purification cycle and one hour prior to the end of the purification cycle.

………………………………………………………………………………………

Instrument used…………………………………………………….

Date last calibrated…………………………………………………..

1st sample mV…………………….

2nd Sample mV……………………

3rd sample mV…………………….

ORPBF mV………………………

Action point mV………………….

| Day, Date and Time | Ozone supplied to system mg/l | ORP at entry to System | ORP at exit of system | Notes | Signature |
| --- | --- | --- | --- | --- | --- |

Annex 2

Purification Tank Operation Record

Tank No. ______________

| Purification Tank Loading | Species |  |
| --- | --- | --- |
|  | Quantity of molluscs | Boxes KG |
|  | Registration Document Nos/ Batch No. |  |
|  | Seawater Use No. |  |
|  | Date of Original Supply of Seawater |  |
|  | Seawater Salinity | ‰ |
|  | Period of UV Use to Date | Hours |
|  | Signature of Operator: |

| During Purification | Start of Cycle | 2 to 3 Hours After Start | Mid- Cycle | End of Cycle |
| --- | --- | --- | --- | --- |
| Date | / /200 | / /200 | / /200 | / /200 |
| Time | : hrs | : hrs | : hrs | : hrs |
| Water Level OK | Yes | No |  | Yes | No | Yes | No |
| Water Flow OK | Yes | No |  | Yes | No | Yes | No |
| UV Lamps OK | Yes | No |  | Yes | No | Yes | No |
| Water Temp. | ºC |  | ºC | ºC |
| Dissolved Oxygen Level |  |  |  |  |
| ORP (Spray bar) |  |  |  |  |
| ORP (suction bar) |  |  |  |  |
| Protein Skimmer |  |  |  |  |
| Water Appearance and Odour OK |  | Yes | No | Yes | No | Yes | No |
| Mollusc Activity OK |  | Yes | No | Yes | No | Yes | No |
| Signature of Operator |  |  |  |  |

| After Purification | Seawater Dumped or Retained | Dumped | Retained |
| --- | --- | --- | --- |
|  | Tank and Containers cleaned | Yes | No |
|  | Cumulative Total of UV Use | Hours |
|  | Signature of Operator: |  |

Comments (Record of breakdowns; spawning in tanks; failure of molluscs to function; addition or change of water; dumping of molluscs; etc) Signature of Operator:

Suggested Addition to HACCP to take account of Ozone etc

| Process Step | Hazards | Controls | CCP | Critical Limits | Monitoring Procedures | Corrective Actions |
| --- | --- | --- | --- | --- | --- | --- |
| Nº. | Ozone Treatment | Production of Brominated by-products | Use Artificial Seawater which has no Bromine salts or if using Natural Seawater use Activated Carbon Filter after ozonation | Y | Ozone delivered to water system not to exceed 0.5mg/LCompliance or redox equivalent ORPBF + 10% in water animals reside in | Use Redox probe to manufacturers and Seafish standards at entry point of water to system and at exit point of system as per Seafish advice | Shut down the ozone generator or its feed line to the purification system. |
| Nº. | Protein Skimming | Unit fails to remove organic matter | Visual check unit is working | N | No excessive foaming on purification tanks. No Faecal matter visible in suspension | Visual checks as per Seafish Purification Tank Operation Record Sheet | Re-establish integrity of water system |